## Slide 1: Modeling Clock Synchronization in the Chess gMAC WSN Protocol Mathijs Schuts Feng Zhu Faranak Heidarian Frits Vaandrager
QFM’09

## Slide 2: Plan
Intro to WSN and Chess case study
Recap of previous results
Our new model
Results
Conclusions

## Slide 3: Chess 2.4 Ghz WSN

## Slide 4: Sensor Network
Interface electronics, radio and microcontroller
Soil moisture probe
Mote
Antenna
Gateway
Server
Internet
Communications barrier
Sensor field

## Slide 5: Sensor Network
Gateway
Server
Internet
Sensor field
Watershed

## Slide 6: Case Study for EU Quasimodo Project
Model and analyze Chess WSN, based on
informal specification in deliverable
discussions with experts

## Slide 7: Our Focus: Clock Synchronization
TX
RX
RX
idle
idle
idle
idle
Time is considered as a sequence of Time Frames.
A time frame is composed of a fixed number (C) of Time Slots.
In a time slot the hardware clock of the sensor node ticks a fixed number (k0) of times.
A Time Frame
tsn
Notes: The Medium Access Control (MAC) layer is responsible for regulating the access to the wireless shared channel. Medium access control is of fundamental importance in sensor networks in order to reduce conflicts as much as possible, thus maintaining the network capacity to a reasonable level. Collision avoidance, energy efficiency, scalability in node density, latency, fairness, throughput, and bandwidth utilization are important attributes of a good MAC protocol.
In the approach of Chess Company, each node takes time as a sequence of time frames, and each time frame is made up of a number of time slots that may be either active or idle. In the active time slots, the node can transmit or receive. A node, can transmit a message only once per time frame in a single time slot called TX slot. On the other hand, the node may receive messages of its neighbor nodes in the other active slots, which are specified for receiving and called RX slots. The TX slot and the RX and idle slots of a node are arranged in a particular order, called TDMA schedule of that node, thus, for each node, each slot is characterized by a type RX slot, TX slot, or idle slot and an order of operation.
We assume that all the active slots of a node are massed in the beginning of a time frame, followed by idle slots. All RX slots are identical and in each of them the node can receive a message from any of its neighbors, and the only TX slot should be scheduled in a way that no communication collision exists between the neighbors.
7

## Slide 8: Goal: Minimalize Energy Consumption
RX Time Slot
TX Time Slot
Guard Time
Guard Time

## Slide 9: Related Work: Our FM Paper
Full parametric analysis for clique networks
Parameter constraints found using Uppaal
Proof fully checked using Isabelle/Hol (> 5000 lines)
Correctness also studied for line topologies

## Slide 10: Related Work: Our FM Paper
Full parametric analysis for clique networks
Parameter constraints found using Uppaal
Proof fully checked using Isabelle/Hol (> 5000 lines)
Correctness also studied for line topologies
Model does not correspond to Chess implementation!

## Slide 11: How Current Implementation Works
Clocks only synchronized once per frame
Implementation computes median of phase errors of all messages received in frame
Offset = median * gain
Radio switching time is relevant

## Slide 12: Structure of Uppaal Model

## Slide 13: Clock

## Slide 14: Sender

## Slide 15: Receiver

## Slide 16: Controller

## Slide 17: Synchronizer

## Slide 18: compute_phase_correction()
if (number of received messages == 0)
offset = 0;
else if (number of received messages <= 2)
offset = the phase error of the first received message * gain;
else
offset = the median of all phase errors * gain

## Slide 19: Invariants for Correctness
“Whenever I send all my neighbors listen”
INV1 : A[] forall (i: Nodes) forall (j : Nodes)
SENDER(i).Sending && neighbor(i,j)imply RECEIVER(j).Receiving
“My neighbors never send simultaneously”
INV2 : A[] forall (i:Nodes) forall (j:Nodes) forall (k:Nodes) SENDER(i).Sending && neighbor(i,k) && SENDER(j).Sending && neighbor(j,k) imply i == j
“There’s no deadlock”
INV3 : A[] not deadlock

## Slide 20: Counterexample found by Uppaal

## Slide 21: Protocol fails for any network that contains 2 clans!
Gateway
Server
Internet
Sensor field
Watershed
Slow nodes
Fast nodes

## Slide 22: How to Fix the Problem?
Assegei (2008) proposed use of Kalman filter instead of median algorithm
Our FM2009 algorithm, possibly with gain factor
Algorithm of Lenzen, Lochen & Wattenhofer (2008)
Adaptation of algorithm Pussente & Barbosa (2009)
It should be easy to adapt our Uppaal model

## Slide 23: Probabilistic Challenges
Probabilistic model of message loss
Probabilistic algorithms for (dynamic) slot allocation
Probabilistic leaving/joining of nodes/networks
Probabilistic algorithms for gossiping
…
Key design issue: independence of layers?!?!!

## Slide 24: Conclusions
Our contribution: Uppaal model of clock synchronization in Chess WSN; serious bug found
Never trust your model!
Demo in preparation
Model checking useful, even if one can only handle trivial instances
Models are imperfect approximations of reality (“Physicists approach to modeling”)

## Slide 25: Questions?
Notes: 25